## Slide 1
Eyedrone
1

## Slide 2
2
TEAM
Albert
Ali
Antonio
Asma
Eva

## Slide 3
Move a drone using your eyes
3

## Slide 4
How?
4

## Slide 5: The end-to-end system
1. Data acquisition, preprocessing and detection
- Get raw data from sensors
- Process in real time
- When a change is detected, send a chunk of data as input to the neural network
2. Classification using AI
- Get movement of the eye as output
3. Drone controller
- Send movement to Drone
- Drone executes the movement
Microservices approach: parts are interchangeable. Example: instead of using eye movements, we could use brain "thoughts", just by changing the first part

## Slide 6: Ganglion Board + Sensors + Open BCI GUI Recording datasets
Usage of Ganglion Board (4-channel EEG) + golden cup sensors.
Recordings made with OpenBCI GUI
Recording example
right eye movement​

## Slide 7: Ganglion Board + Brainflow + Timeflux
Raw data acquisition directly from board for real –time detection

## Slide 8: Unfortunately, there are some parts missing:
What is missing? Real Time processing.
Get chunks of data in real time when an event happens (not only the event) and pass this as an input to the Neural Net. Making this work in real-time was not an easy work.
Pass the output of the neural net to the Drone API in real time.
Investigate REST vs Websockets to connect with the drone.

## Slide 9
Dataset

## Slide 10: Dataset creation
Using OpenBCI Ganglion Board (4-channels)
Tests done: 25x Center --> Up --> Center movement 25x Center --> Down --> Center movements 25x Center --> Left --> Center movements 50x Center --> Right --> Center movements 1x Long Blinking Test

## Slide 11
Main problems...
Lack of data
We wanted to:
-Have multiple sources of data
-From each have multiple recordings
-Do data augmentation

## Slide 12
Learning
01
02
03
Data Augmentation
Machine Learning
Deep Learning

## Slide 13: Data Augmentation
Concept:
Choose randomly P% of time points;
Stretch them with[Min-Max]s
Helps:
Less biased model;
Generated Noise;
Concept:
Choose randomly P% of time points;
Stretch them with[Min-Max]s
Helps:
Less biased model;
Generated Noise;

## Slide 14: Machine Learning: SVM
DOWN
RIGHT
UP
LEFT
CENTER
Feature Vector:
Mean, Max , Min , Var;
5 classes
Result:
43% accuracy

## Slide 15: Deep Learning: EEGNet
Fully supervised
Few data
Compact architecture
Engineering
EEGNet: A Compact Convolutional Neural Network for EEG-based Brain-Computer Interfaces Vernon J. Lawhern1, Amelia J. Solon, Nicholas R. Waytowich, Stephen M. Gordon,Chou P. Hung, and Brent J. Lance

## Slide 16: Deep Learning: EEGNet
Training and Engineering:
Number of channels 4
Frequency 100Hz
Result:
50,1% accuracy

## Slide 17: THE DRONE
Communications
DroneApp connected with the Drone API
Real time show
Flask app for simple navigation controller
Router port forwarding to be able to work remotely

## Slide 18
Progress
Dataset creation: Collect EEG signal with 4 golden cup sensors
Done
Signal sending:
in real-time from a Board to PC and/or Cloud (Amazon Web Services)
Signal/data pre processing: Data cleaning, noise
Done
API Drone
Classification:
Data augmentaion Done
SVM Done
Deep learning On-going
01
02
03
04
05
5